PUBLIC INVITATION TO TENDER

Background

Health for All Project in Albania (HAP) is funded by Swiss Agency for Development and Cooperation (SDC) of the Swiss Government and is being implemented by Health for All Centre in Fier and Diber Regions. Its overall goal is that the Albanian population, including the most vulnerable, benefit from better health due to improved primary health care services and health promotion activities.

In this frame HAP is supporting the Master in Health Management and is seeking offers to purchase the below items. They will be delivered in Tirana at the University of Medicine.

| No | IT Equipment | Units | Notes |
| --- | --- | --- | --- |
| 1 | Desktop PC | 4 |  |
| 2 | UPS for the desktop PC | 4 |  |
| 3 | Projector | 6 | 5 mounted in the classrooms, one mobile |
| 4 | Photocopier | 1 |  |
| 5 | Projection Screen | 5 | mounted in the classrooms |
| 6 | IBM SPSS Base v25 perpetual license | 2 | 2 single user licences |

# The following section details the minimum technical specifications for the IT equipment:

## The bidders should provide:

## Manufacturer Authorization Form (MAF) for the offered products

## Certification of  IT staff

## Guaranty of 1 year for equipment.

## Desktop PC

| Minimal requirements |  |
| --- | --- |
| Processor rating (cpubenchmark.net) | 6500 |
| RAM | 16 GB DDR4 ECC |
| HDD | 2 x 500 GB, 7200 rpm SATA |
| Graphics subsystem | Dedicated card min 1 GB memory |
| Communication ports | USB: min 3 ( 2 upfront),RJ-45,audio in/out, mic and headphone,VGA |
| Networking | 10/10/1000 LAN Gigabit Ethernet |
| Sound card | included |
| Speakers | Internal or built-in monitor |
| OS preinstalled, licensed, activated | OEM Windows 10 64-bit Proffesional |
| Keyboard | Standard QWERTY |
| Mouse | 3-button optical scroll |
| Power Supply | 220V/50Hz |
| Power cord | European |
| Recovery | Recovery CD/DVD or recovery partition |
| Monitor | LED/LCD , compatible and same brand as the PC 23 inch,1920x1080@60Hz native resolution, <= 5 ms response time,1000:1 contrast ratio, Display port: one VGA or DVI, one from DVI/HDMP/DP Power supply : 220V /50 Hz Power cord: European |
| Preinstalled software | Antivirus Software with at least 1 year updates subscription |
| Documentation | Printed or electronic in English language |
| Warranty | 1 year for the PC unit, one year for the monitor |

The contractor should also install cable channels/raceway for the internet cable for the two PC’s of the secretaries, in the office in the entrance, and mount the existing mini-switch on the wall.  An estimated 10 m length of cable + cable channels/raceway will be needed.

## UPS for the desktop PC

| Minimal requirements |  |
| --- | --- |
| Power | 1000 VA |
| Power factor | >=0.5 |
| Wave form | sinusoidal |
| Output Nominal voltage | 220-240 VAC |
| Output Frequency | 50 Hz +/- 5% |
| Voltage regulation on battery | +/- 10% |
| Output connectors | >= 4 IEC 320 |
| Input voltage (nominal) | 220-240 VAC |
| Input Voltage range | 170-270 VAC |
| AVR | yes |
| Input connectors | 1 IEC 320 |
| Automated shutdown software | included |
| Led indicators | yes |
| Audible indicators | yes |
| Data port | USB or DB9 serial |
| Protection | Overload, discharge and overcharge |
| Transfer time | <= 4 ms |
| Back-up time | >= 6 min full load |
| Battery type | Lead acid |
| Power cord | 1 European IEC –C13 2 European IEC –C14 |
| Data cable | DB9-DB9 or USB-USB |
| Documentation | Printed or electronic in English language |
| Warranty | 1 year |

## Projector

| Minimal requirements |  |  |
| --- | --- | --- |
| Type |  | Full HD |
| ANSI Lumen |  | 4000 |
| Resolution |  | 1920x1080 |
| Input signal |  | NTSC/PAL |
| Lamp life |  | 4000 hours |
| Contrast ratio |  | 3000:1 |
| Lens adjusting |  | F number, Zoom manual,Focus manual/automatic |
| Input terminal |  | HDMI/VGA/COMPONENT/COMPOSIT/S-video |
| Power cord |  | European |
| Remote control |  | Yes |
| Video cable |  | 1 HDMI-HDMI 1 VGA- VGA 1 RCA- RCA 1 S-Video -- S-video |
| Connectivity over Wi-Fi |  | Included ( native or wireless dongle/adapter) |
| Lens cap |  | yes |
| Software CD |  | yes |
| Documentation |  | Printed or electronic in English language |
| Projector screen |  | Manual, with auto-lock, minimum size: 180cm x 180 cm |
| Warranty |  | 1 year |

The contractor shall deliver, assemble, install and prepare the projector for work, including the connection to the local WI-Fi network and train the IT staff in its use. The contractor shall include the needed ceiling mounts and all other accessories needed for mounting the 5 projectors in the ceilings, and also mount the 5 projector screens in each of the five classrooms. The contractor shall install the projector screen on the wall facing the projector, shall install also a VGA cable for each connection videoprojector-laptop in order to make the presentations, with appropriate cable channels/raceways. An estimated 10 m length of cable will be needed, assuming that the laptop will be used from the lecturer’s table.

## Photocopier B&W

| Minimal requirements |  |
| --- | --- |
| Model | Copier/Printer/Scanner |
| Copy/print speed for A4 | >= 25 ppm |
| Monthly duty cycle | 60,000 pages |
| Technology | Laser B&W |
| Reduction/Enlargement | 25% - 400% |
| Document feeder | DADF/RDF |
| Input capacity | 2000 |
| Output capacity | 250 |
| Dublex copying/printing | yes |
| Media Size | A3/A4 |
| Interface | High speed USB 2.0 Ethernet |
| Power cord | European |
| Software drivers | Yes |
| Compatibility | Windows 10 Professional |
| Power supply | 220 V, 50 Hz |
| Documentation | Printed or electronic in English language |
| Warranty | 1 year or 150.000 pages |

The contractor shall deliver, assemble, install and prepare the copier for work, including the supply and installation of toner and train the office staff in its use. The staff should as a minimum be trained how to perform copying, printing and scanning.

# The following section details the technical specifications for the licensed SPSS Base V25:

- Single-user, desktop application for Windows and Macs. Includes 12 months of technical support.

- Read/write text, Excel, SAS, and more; no size limits

- Descriptive statistics, data prep, and graphing

- Programmability/extensibility; supports R/Python

- Bivariate statistics procedures, factor and cluster analysis

- Linear and ordinal regression

- Basic reporting with export to Microsoft/PDF

- Software should be in original CD/DVD

You should also include in your offer:

- Quotation (price without VAT)

- Delivery date

- Registration of the company. (NIPT, etc)

- Previous experience of the company

- Offers should be signed and stamp

The offers must be delivered by 24 November 2017, in sealed envelopes and with clearly marked “Public Invitation to Tender for IT equipment” to;

HAP Centre

Procurement Team

Street “Themistokli Gërmenji”,

Pall.10, Kati II, Apt.1

Tirana, Albania